## Slide 1: Using Trees to Help Mitigate Tropospheric Ozone Levels and Stormwater Runoff in Desoto County
Eric Kuehler
Technology Transfer Specialist
USDA Forest Service
ekuehler@fs.fed.us
706-559-4268
Notes: The purpose of this meeting is to (1) share results of the Desoto County forest assessment project conducted in 2010 to be used as baseline data, (2) convince the county that management of their forest resources could help to manage stormwater runoff and mitigate air quality concerns, and (3) list potential management strategies to use natural processes to help reduce the county’s tax burden.

## Slide 2: Why Retain Forest Lands?
What do forests do for us?
  Reduce ambient air temperature
  Slow down rainfall
  Filter stormwater
  Air filtration
    Particulates
    pollutants
  Provide recreation to residents
Notes: Forest systems are vital for clean water and air. New York City thinks so much of this that they pay to manage watersheds in the Pocono Mountains in order to have clean drinking water for its citizens.

## Slide 3: Why do we plant trees in cities?
Aesthetic beauty?
Environmental services
Notes: When we think about planting trees in our developed areas like cities, we think about their aesthetic beauty. But trees provide so much more to us in the form of environmental services. We should begin to think about using trees to help us address environmental issues cities are faced with. As Desoto County’s population increases and the land is developed, trees can play a vital role in ensuring water and air quality.

## Slide 4: What are Environmental Services?
Services provided naturally with no direct costs
Energy Conservation
  Shade / wind break
  Reduced ambient air temperatures
    Lower heat island effect
Stormwater interception
  Reduced flow rate
  Help mitigate stormwater problems
Notes: Environmental services are those services that trees provide to us naturally that improve our quality of life. We don’t pay for these services directly.
Trees help to reduce stream flow flashiness that can reduce stream erosion. Trees can also help to keep stream water cool for its biota.

## Slide 5: What are Environmental Services?
Pollution removal
  Particulate matter
    Soot
    Dust
  Gaseous matter
    NO2, SO2, O3, CO
Carbon Storage
  Stem
  Roots
Carbon sequestration
  Removal of CO2 from air
Notes: Trees remove pollution directly through dry deposition or uptake and indirectly by cooling our environment thus reducing energy generation and volatile emissions.

## Slide 6: Other Benefits of Urban Trees
Increased business income
Increased property values
Reduced asphalt replacement
Traffic calming
Natural UVA/UVB protection
Safer walking environments
Improved overall health
Natural screen/filter
Improved Quality of Life
Notes: Research has shown that strategically-placed and well-maintained trees can provide many more benefits to a city that can improve the quality of life for its residents and visitors.

## Slide 7: How do trees provide these services?
The greater the leaf area the greater the services
How can we quantify these services and the value of urban trees to society?
Notes: Leaf area is the key to environmental services.

## Slide 8: i-Tree
Suite of public domain urban forest analysis and benefits assessment software
  www.itreetools.org
Released to the public in 2006
Quantifies structure, environmental benefits, and monetary value of community trees
Helps communities better manage their natural resources
Notes: A suite of urban forestry software applications developed by Forest Service researchers helps a community quantify the benefits their trees provide.

## Slide 9: i-Tree Suite of Software Tools
i-Tree Streets
  Street tree cost/benefit analysis model
i-Tree Storm
  Pre- / Post-storm debris estimation model
i-Tree Hydro (new to Version 4)
  Stream flow / water quality simulation model
i-Tree Vue
  Urban tree canopy / environmental benefits tool
i-Tree Canopy (on-line tool)
  Urban tree canopy estimation tool
i-Tree Eco
  Urban tree/forest structure, function, value model
Notes: The i-Tree tools are designed to look at various aspects of a community’s urban forest. For this project, we used i-Tree Vue, Canopy, and Eco to assess Desoto’s forests and their value.

## Slide 10: Desoto County i-Tree Vue Project
i-Tree Vue used to get a quick look at forest canopy percentage and estimated benefits
based on 2001 NLCD dataset
  Landsat imagery @ 30 m2 resolution
Pollution removal estimated based on leaf area assumptions

## Slide 11: Desoto County i-Tree Vue Project
Notes: Using NLCD 2001 imagery for land cover, impervious surface cover and canopy cover, we were able to estimate county-wide canopy cover and the pollution removal benefits from that canopy. As well as break it down by land cover classes.
Imagery was downloaded from MRLC
Using county boundary layer provided by county GIS, imagery was clipped and imported into the tool
Results for tree canopy and impervious surface cover by land cover type were exported
Pollution removal due to tree canopy cover was estimated by the tool and exported.

## Slide 12: Desoto County i-Tree Vue Project
Desoto County = 329,335 ac
  Developed = 13%
  Forest = 33.7%
  Wetlands = 7.6%
  Agriculture = 39.9%
  Water = 5.2%
  Other = 0.5%
    Barren land (rock, sand, clay)
    Grassland / herbaceous
Notes: From the 2001 imagery and the Vue model, we estimate that 13% of the county is developed, 34% is forested, 8% is wetlands, 40% is agriculture, and 5% is open water.

## Slide 13: Desoto County i-Tree Vue Project
Entire county
  330,000 total acres
  Tree canopy cover = 30%
  Impervious cover = 3%
Pollution removal annually
  CO2 = 125,000 tons
  Ozone = 2100 tons
  NO2 = 400 tons
  SO2 = 175 tons
  PM10 = 1000 tons
Developed land cover class
  43,000 total acres
  Tree canopy cover = 16%
  Impervious cover = 23%
Pollution removal annually
  CO2 = 9,300 tons
  Ozone = 150 tons
  NO2 = 28 tons
  SO2 = 14 tons
  PM10 = 77 tons
Canopy cover and benefits based on 2001 imagery
Notes: For the entire county area, Vue estimates 30% tree canopy cover and 3% impervious surface cover. From that canopy cover, we estimate this amount of pollution removal.
The developed land cover type makes up 13% of the county and of that, only 16% is covered by tree canopy. Pollution removal by trees in developed areas is much less.
Remember, this canopy cover and benefits are based on 10 year old data. So we can use another i-Tree tool to better estimate current canopy cover and use the canopy change function in Vue to fine tune these benefits estimations.

## Slide 14: Desoto County i-Tree Canopy Project
Notes: We then used i-Tree Canopy to get a more current look at the canopy cover for Desoto County using Google Earth imagery.
How this works is, You will load a boundary shape file projected in decimal degrees into the tool, and then i-Tree Canopy randomly places points within your area of interest.
For each of those points, you judge whether it falls on canopy or whatever attribute you are interested in.
Generally, you will need over 500 random points for statistical precision.

## Slide 15: Desoto County i-Tree Canopy Project
Notes: We assessed 500 random points for tree canopy cover, impervious surface cover, pervious surface cover, and open water. This graphic shows the locations of each point and the assessed attribute.

## Slide 16: Desoto County i-Tree Canopy Project
i-Tree Vue
  Tree canopy = 30%
  Impervious cover = 3%
  Water = 5.2%
i-Tree Canopy
  Tree canopy = 34%
    +/- 2.12
  Impervious cover = 6%
    +/- 1.06
  Water = 6.6%
    +/- 1.11
Notes: Comparing our 2001 Vue results with the more recent Canopy results, we see that the numbers are fairly close.
Because the pixel size for Vue is 30 square meters, it tends to under-estimate features, and that is evident here.
We can now take our more current canopy values and use them in a Vue canopy change scenario to fine-tune the environmental services numbers.

## Slide 17: Desoto County i-Tree Eco Project
15 original strata
  Using 2001 NLCD
Combined strata
  Cultivated crops
  Forest
  Developed
    Residential
    Commercial
    Industrial
  Developed open space
    Parks/golf courses etc.
  Herbaceous
  Wetlands
Notes: i-Tree Vue and Canopy gave us preliminary data to help us justify the next phase of the project. Data collection for i-Tree Eco is much more involved because it requires field measurements. i-Tree Eco uses a sampling methodology to estimate forest structure and calculate environmental services. Using 2001 national land cover classifications, 15 different land cover types were identified in Desoto county. Interpreting results for that many different strata would be difficult, so we decided to combine similar land cover types. We ended up with six strata from which to interpret the results.

## Slide 18: Desoto County i-Tree Eco Project
290 random plots stratified by land use
Plots fell on private and public lands
  Back yards
  Parks
  Vacant lands
1/10th acre circular plots
Inventory every tree on plot
  MS State Forestry
Notes: We randomly placed 290 plots around the county segregated by land cover type. Each stratum had at least 30 plots. Because they were randomly located, plots fell on public and private property. Each plot was measured to cover an area of 1/10th acre. Every tree was identified to species on each plot by MSU forestry students and measured for stem diameter, height, crown diameter, and other crown parameters.

## Slide 19: Desoto County i-Tree Eco Key Findings
Data were extrapolated to estimate benefits
  Desoto County ≈ 330,000 acres
  Developed land cover type ≈ 15%*
  Agricultural ≈ 39%
  Forests ≈ 32%
  Wetlands/water ≈ 13%
  Tree canopy cover ≈ 27% per i-Tree Eco
* Based on 2001 NLCD
Notes: The i-Tree model extrapolated those data to estimate forest structure and calculate function and value. Based on 2001 national land cover dataset these are the percentages that make up the county. Based on the data collected and model estimates, the entire county has about 27% tree canopy cover. This seems to be underestimated compared to the Vue and Canopy results, but this may be a result of sampling error.

## Slide 20: Leaf Area = Benefits
Chart: Square feet of leaf area/Ac
| Cultivated Crop | Developed | Forest | Herbaceous | Open_Space_Dev | Wetlands | TOTAL AREA
 | 17417.03 | 29455.71 | 245769.44 | 39520.25 | 88052.62 | 60514.42 | 85073.55
Notes: Environmental services or benefits are dependent on leaf area. As expected, forested land cover provides the greatest leaf area. The developed land cover type where most of the ozone and pollution is generated, has a very low leaf area concentration. We would expect tree leaf area to be low in cropland and hay fields, but the low leaf area in developed land use is alarming. A strategy would be to encourage parcel owners in developed land use areas to strategically plant trees to shade buildings and impervious surfaces.

## Slide 21: Desoto County i-Tree Eco Project
Key findings
  Number of trees = 19 million
  Most common species
    Sweetgum (19%)
    Winged elm (12%)
    Green ash (5%)
    Loblolly pine (5%)
  Total rainfall interception
    1.14 billion gallons/yr
    $10.2 M/yr
  Pollution removal = 3500 tons/year ($17 M/yr)
Notes: Some trees actually emit precursors to ozone formation. Sweetgum and pine are two such species. Unfortunately, in the South, we have a lot of sweetgum and pine that are pioneer species and colonize abandoned fields. Their leaf area fortunately provides an abundant amount of shade to offset the deleterious effects.

## Slide 22: Desoto County i-Tree Eco Project
Annual rainfall interception
Land Use | Leaf Area (mi2) | Rainfall interception (ft3/yr) | Value ($0.067/ft3)
Cultivated cropland | 54.5 | 8.5 M | $573 K
Developed | 18.3 | 2.9 M | $192 K
Forest | 623.8 | 97.8 M | $6.6 M
Herbaceous | 111.2 | 17.4 M | $1.2 M
Open_space Developed | 74.2 | 11.6 M | $780 K
Wetlands | 88.4 | 13.9M | $928 K
Total | 970.4 | 152.1 M | $10.2 M
Total rainfall interception = 1.14 Billion gallons per year
Notes: Using $0.067 per cubic foot of water, the trees in Desoto provide approximately $10 million in avoided costs by intercepting rainfall.

## Slide 23: Desoto County i-Tree Eco Key Findings
Key findings related to pollution
  Estimated Total removal = 3500 tons/year
  O3 removal = 2500 tons/yr
  CO removal = 85 tons/yr
  NO2 removal = 375 tons/yr
2011 Desoto County monitoring station
  NOx = 5080 tons
Trees directly remove about 7% NOx annually
Notes: Regarding pollution removal, i-Tree Eco calculated that 19 million trees in the county remove about 3500 tons of pollution annually. The majority of which is ozone. Compared with the 5000 tons of NOx reported in Desoto County in 2011, trees directly removed about 7%.

## Slide 24: Reducing Photochemical Reaction
Photochemical oxidant cycle
  NO2 + VOC O3
  Increased ambient air temperatures increase rate of reaction
Ozone levels have been shown to be reduced under tree canopy
  Harris and Manning (2010)
The larger role for urban trees?
  Reduce sunlight and temperature via shade
Notes: Ozone formation is a result of NO2 and organic compounds reacting via solar energy in the photochemical oxidant cycle. Elevated ambient air temperatures increase the rate of this reaction. Research has shown that ozone levels under urban tree canopy are lower than levels not under canopy. The larger role for urban trees is to prevent the formation of ozone by blocking sunlight and reducing air temperature. However, these direct and indirect strategies could work together for an effective ozone reducing system.

## Slide 25: Recommendations for Mitigating O3
Retain/increase canopy cover where possible
  Reduces solar light levels
  Reduces urban heat island effect
Strategically plant trees around
  Buildings
  Parking lots
  Roads
Plant large, long-lived, low maintenance trees
  Natives and low BVOC emitters
Encourage citizens to plant on their parcels
Notes: So we recommend that healthy trees be retained where possible and consider developing tree canopy cover goals in developed areas of the county to help reduce solar energy and air temperature.
Strategically plant trees around buildings to reduce their need for electricity that will also help to reduce emissions at the power plant. Shading parking lots and roads will also help to reduce air temperature.
Larger trees provide more benefits. To reduce emissions caused from maintenance, plant long-lived and low maintenance trees. Trees known to emit biogenic voc’s should also be avoided.
And encourage homeowners to strategically plant large trees around their house and on their property for the same reasons.

## Slide 26: i-Tree Tools Conclusion
So how can we use this information?
  Planning for future development
    Where to develop
  Developing green infrastructure policy
    Canopy cover goals
    Carbon storage and sequestration plans
    Pollution mitigation plans
    Stormwater plans
  Managing the forest to maximize benefits

## Slide 27: Using Trees to Help Mitigate Tropospheric Ozone Levels and Stormwater Runoff in Desoto County
Eric Kuehler
Technology Transfer Specialist
USDA Forest Service
ekuehler@fs.fed.us
706-559-4268